## Slide 1: Perceptual Visibility Prediction of Overlaid Content in Optical See-Through Augmented Reality
光学シースルー拡張現実における 重畳コンテンツの知覚的視認性予測
Oishi-Lab M2 Kazuki Hamada
Department of Electrical Engineering and Information Systems
Graduate School of Engineering, The University of Tokyo
2026/05/15

## Slide 2: Outline
1. Introduction
2. Related Work
3. Method
4. Pilot Experiment
5. Conclusion & Future Work

## Slide 3: Outline
1. Introduction — background, scope, objective
2. Related Work
3. Method
4. Pilot Experiment
5. Conclusion & Future Work

## Slide 4: Introduction: Optical See-Through AR
A virtual image is optically overlayed
on the real-world background
Pros:
Direct perception of real world
Cons:
Additive mixture of FG & BG
Real BG
Virtual Object
Beam Splitter
Monitor

## Slide 5: Introduction: Visibility Depends on the Background
Visibility of overlayed content varies depending on backgrounds
→ Need to predict visibility from the FG/BG image
High visibility
Low visibility
→Bad UX, Safety

## Slide 6: Scope & Objective
Goal: Build an image-based visibility predictor for OST-AR
Three steps
1. Psychophysical Experiment : Reveal HVS mechanism
2. Model Extension: From 2D to OST-AR
3. Model Validation: model's predictions vs human ratings

## Slide 7: Outline
1. Introduction
2. Related Work — four topics
3. Method
4. Pilot Experiment
5. Conclusion & Future Work

## Slide 8: Related Work (1): Contrast Perception
Visibility ← Contrast Perception | Two phenomena addressed
Contrast
Spatial frequency
① Frequency dependence (CSF)
② Contrast masking
→This work mainly focus on ② contrast masking
[1] Fukiage et al. “Visibility-based blending for real-time applications” 2014
[1]

## Slide 9: Related Work (2): Single-Factor Models for OST-AR
Existing models each consider one perceptual factor
Perceptual factor | Reference
Color | Yoon et al., 2017・Zhang et al., TVCG 2022
Luminance/Illuminance | Liu et al., ISMAR 2022
Transparency | Zhang & Murdoch, 2021
→ No unified, multi-factor model exist

## Slide 10: Related Work (3): IQA for OST-AR Visibility
IQA closely relates to visibility — also in existing-model limits
→ OST-AR-specific perception must be modeled.
Limitation of existing IQA models
OST-AR specific contrast perception
[1]
[2]
[1] Chapiro, et al. “AR-DAVID: Augmented Reality Display Artifact Video Dataset.” 2024
[2] Kim et al. “Supra-threshold Contrast Perception in Augmented Reality.” 2025

## Slide 11: Related Work (3): Fukiage‘s Visibility Predictor
Visibility predictor for α-blended content — promising for OST-AR
→ But some gaps remain when applied to OST-AR
! Considers multiple perceptual factors jointly
[1] Fukiage and Oishi. “A Content-adaptive Visibility Predictor for Perceptually Optimized Image Blending,” 2023
[1]

## Slide 12: Related Work (4): Fukiage‘s Visibility Predictor
The model assumes α-blending — single 2D display
Four OST-AR specific gaps:
1. Accommodation: induces defocus blur
2. Binocular disparity: arises with depth difference
3. BG discounting: observers partly ignore the real BG
4. Optical addition: HDR-range output
→ This work bridges these gaps, extending the model to OST-AR

## Slide 13: Outline
1. Introduction
2. Related Work
3. Method — overview & three steps
4. Pilot Experiment
5. Conclusion & Future Work

## Slide 14: Method: Overview
STEP 3 Model Validation
— Compare with human rating
STEP 1 Visibility Evaluation Experiment
— Quantify perceptual effects on visibility
STEP 2 Model Extension
— Extend input processing from results
Three steps to extend Fukiage’s model for OST-AR

## Slide 15: Method (1): Visibility Evaluation Experiment
Linear summation
Contrast perception
change
BG perception change
Defocus + Binocular disparity
BG discounting
Non-optical perception change
Quantify how each OST-AR specific factor affect visibility
→Decide extensions & fit parameters
[1]
[1] Kim et al. “Supra-threshold Contrast Perception in Augmented Reality.” 2025

## Slide 16: Method (2): Model Extension
Extend model pipeline with four OST-AR-specific mechanisms
① Defocus blur (Calculate PSF)
② Disparity & combination
Geometric computation
& existing-model selection
③ HDR → SDR (Tone mapping)
④ Background discounting
Fit the attenuation process
[1]
[1] Reinhard et al. “Photographic tone reproduction for digital images.” 2022

## Slide 17: Method (3): Model Validation
Evaluate the model by comparing with human evaluation
Psychophysical experiment
Visibility evaluation in OST-AR, using general texture images.
Model Evaluation
Quantitatively compare human scores with model predictions
(e.g., R², SROCC)

## Slide 18: Outline
1. Introduction
2. Related Work
3. Method
4. Pilot Experiment — design, results, discussion
5. Conclusion & Future Work

## Slide 19: Pilot Experiment: Objective
Identify the parameters & conditions for the main experiment
Quantify how defocus blur & uncrossed disparity affect visibility,
across:
Stimulus parameters
Spatial frequency
FG / BG luminance
BG contrast
Viewing conditions
Diopter difference
Ocularity

## Slide 20: Pilot Experiment: Apparatus
Optical components
Beam splitter: T 20–30%, R 50–60%
2× 27" LCD, 2560×1440
Luminance
FG max: 100 cd/m²
BG max: 30 cd/m²
Viewing geometry
Chin rest, dark room
70 ~ 150 cm
50 ~ 130 cm
Wall
Background
LCD display
Foreground
LCD display
Beam splitter
Forehead Support

## Slide 21: Pilot Experiment: Procedure
Rating scale
1 Invisible — 5 Very clear
Stimulus pairing
Reference: Gabor patch
Test: Gabor + BG noise
Trials
All combinations × 2 repeats
Randomized
N = 1 observer (author)
0.0
1.0
1.5
2.5
t(s)
FG
BG
Real
Ref
Test
BO

## Slide 22: Pilot Experiment: Stimuli
Specification | Value
Stimuli size | 7.9°× 7.9°
Envelope of Gabor patch (σ) | 1°× 1°
Spatial frequency (SF, cpd in Gabor patch) | 2, 4, 6, 8 cpd
Foreground luminance(YFG) | 50 cd/m² or 5 cd/m²
Background luminance(YBG) | 15 cd/m² or 5 cd/m²
Foreground contrast(CFG) | 1.0
Background contrast(CBG) | 1.0 or 0.0

## Slide 23: Pilot Experiment: Conditions
Pair num | dFG [m] | dBG [m] | DFG [D] | DBG [D] | ΔD [D]
1 | 0.50 | 0.70 | 2.00 | 1.43 | 0.57
2 | 0.81 | 1.50 | 1.23 | 0.67 | 0.57
3 | 0.50 | 1.00 | 2.00 | 1.00 | 1.00
4 | 0.60 | 1.50 | 1.67 | 0.67 | 1.00
Other conditions
Monocular (no disparity) vs Binocular (disparity & combination)
※Defocus blur arise over 0.3 D

## Slide 24: Pilot Experiment: Results — Monocular
Key observations
Strongest degradation at (a)(b)
No consistent ΔD trend
(a) {YFG,YBG} ={5.0,5.0} [cd/m²]
(b) {YFG,YBG} ={5.0,15.0} [cd/m²]
(c) {YFG,YBG} ={50.0,5.0} [cd/m²]
(d) {YFG,YBG} ={50.0,15.0} [cd/m²]
Low SF (2–4 cpd) more affected
Some negative scores
SF
Pair num
0.57 D
1.00 D

## Slide 25: Pilot Experiment: Results — Binocular
(a) {YFG,YBG} ={5.0,5.0} [cd/m²]
(b) {YFG,YBG} ={5.0,15.0} [cd/m²]
(c) {YFG,YBG} ={50.0,5.0} [cd/m²]
(d) {YFG,YBG} ={50.0,15.0} [cd/m²]
Key observations
Luminance, SF, negative scores patterns same as monocular
No consistent ΔD trend
No mono-bino difference

## Slide 26: Pilot Experiment: Discussion
Four redesign directions for the main experiment
① Drop weak masking conditions
Discrete rating lacks resolution where the true effect is small
Fix luminance & spatial freq
High YBG, mid YFG, and low SF
→reduce other axes
Switch to matching method
Use slower, but more accurate method than discrete rating
④ Add single-plane condition
Simulate
linear addition & defocus blur

## Slide 27: Outline
1. Introduction
2. Related Work
3. Method
4. Pilot Experiment
5. Conclusion & Future Work

## Slide 28: Conclusion & Future Work
Conclusion
Goal: extend Fukiage’s visibility predictor to OST-AR through an experiment
Pilot experiment: design study for that experiment
Pilot result: identified the key factors and parameter ranges to target
Future Work
Model Extension & Validation
Add pre-experiment
to check redesign
Main experiment
after ethical review